## Slide 1
GENIE AGENT
Analyze Mode
Complete Flow Guide
From run instruction to analysis report
CDC/RDC · Lint · SpgDFT · Auto-Fixer Loop
4
Entry Points
4
Pipeline Waves
5
Max Fixer Rounds
0
Waivers Added

## Slide 2: Why Analyze Mode?
Too Many Violations
Hundreds of CDC/RDC, Lint & SpgDFT violations —
manual review is slow and error-prone.
Tool Noise vs Real Bugs
DFT/RSMU false positives buried with real RTL issues —
engineers waste time on irrelevant violations.
No Memory Across Re-runs
Fix one violation, re-run, repeat — no tracking of what
was tried before across rounds.
The Solution
→ Automated parallel agent analysis
→ Intelligent filtering — DFT/RSMU excluded
→ RTL-level root cause per violation
→ Auto-apply fixes — constraint & RTL
→ Round-to-round fix memory
→ HTML report emailed per check type
→ ZERO waivers — fixes in RTL or constraints

## Slide 3: 4 Ways to Trigger Analysis
A
Run + Analyze
--analyze
Run static check AND analyze when it
completes. Background monitor keeps
main session free.
B
Analyze Only
--analyze-only
Skip re-running — analyze an already-
completed run. SKIP_MONITORING=true
jumps straight to agents.
C
Run + Auto-Fix Loop
--analyze-fixer
Run → analyze → auto-apply all fixes
→ rerun. Loops up to 5 rounds or until
violations reach zero.
D
Fix Existing Results
--analyze-fixer-only
Start the fixer loop from an already-
completed run. No re-run needed — picks
up where analysis left off.

## Slide 4: The 4-Wave Analysis Pipeline
WAVE 1
Extractor &
Precondition
5 agents in parallel
CDC Precondition · CDC Extractor
Lint Extractor
SpgDFT Precondition
SpgDFT Extractor
▶
GATE
Skip Logic
Gate
If focus_violations == 0
→ skip RTL analyzers
→ mark as CLEAN
in report
▶
WAVE 2
RTL Analyzer
Agents
Parallel — one per violation
CDC · RDC · Lint · SpgDFT
Library Finder
RTL trace + fix formulation
▶
WAVE 2.5
Fix
Consolidator
Deduplicate across agents
Resolve instance vs module
Verify tech-cell traces
Unified fix set
▶
WAVE 3
Report &
Email
3 compilers in parallel
3 HTML files generated
3 separate emails sent
per check type
📁 File-based storage — all intermediate results written as JSON → survives context interruption

## Slide 5: Wave 1 — Extractor & Precondition Agents
CDC/RDC
Precondition
haiku
Reads cdc_report.rpt
& rdc_report.rpt
→ Inferred clocks/resets
→ Unresolved modules
→ Blackbox modules
→ Reads constraint file
CDC/RDC
Extractor
sonnet
Reads CDC Section 3
& RDC Section 5
→ ERROR violations only
→ Filters DFT/RSMU
→ 2-3 per bucket
→ All types covered
Lint
Extractor
sonnet
Reads leda_waiver.log
→ Error violations only
→ Filters rsmu/dft
→ Up to 10 focus
→ Groups by RTL file
SpgDFT
Precondition
haiku
Reads moresimple.rpt
(blackbox section only)
→ BlackboxModule entries
→ Module names
→ needs_library?
SpgDFT
Extractor
sonnet
Reads spec file (not rpt)
→ Pre-computed filter
→ Summary table
→ Unfiltered Error
Details section
All 5 agents run in PARALLEL → Writes: data/<tag>_precondition_*.json & data/<tag>_extractor_*.json

## Slide 6: Skip Logic Gate — Intelligent Agent Skipping
After Wave 1, Claude evaluates each check before spawning RTL analyzers. Zero-violation checks are skipped — no wasted compute.
CDC
focus_violations == 0
→
✓ CDC CLEAN
→
Skip CDC RTL Analyzers
RDC
focus_violations == 0
→
✓ RDC CLEAN
→
Skip RDC RTL Analyzers
Lint
focus_violations == 0
→
✓ Lint CLEAN
→
Skip Lint RTL Analyzers
SpgDFT
focus_violations == 0
→
✓ SpgDFT CLEAN
→
Skip SpgDFT RTL Analyzers
Library
unresolved == 0 &
blackbox == 0
→
✓ No missing libs
→
Skip Library Finder
⚠ Precondition agents are NEVER skipped — even a 'zero inferred' result belongs in the report

## Slide 7: Wave 2 — RTL Analyzer Agents (Parallel)
CDC/RDC RTL
Analyzer
haiku
→ Checks LEARNING.md first
→ Finds RTL file via grep
→ Understands clock domains
→ Traces to leaf tech cell
→ Reads constraint file
→ WHY statement formulation
→ Risk: HIGH / MED / LOW
→ Fix: rtl_fix / constraint
/ investigate
→ ZERO waivers
Lint RTL
Analyzer
sonnet
→ Checks lint/LEARNING.md
→ ONE agent per RTL FILE
→ (not per violation)
→ Reads full RTL file
→ Checks waiver file (ctx)
→ Fix: rtl_fix — real bug
→ Fix: tie_off — debug port
→ Fix: investigate
→ ZERO waivers
SpgDFT RTL
Analyzer
sonnet
→ Checks spgdft/LEARNING.md
→ Identifies violation type:
async → PIN_CONSTRAINT
clock → SGDC constraint
undriven → tie-off
→ Reads project.params
→ Fix: rtl_fix / tie_off
→ Fix: SPGDFT_PIN_CONSTRAINT
→ Fix: sgdc_constraint
Library
Finder
haiku
→ Only if unresolved or
→ blackbox modules found
→ Finds lib.list manifest
→ Searches library files
→ grep -l 'module <name>'
→ Returns: lib path,
→ already in lib.list?

## Slide 8: Wave 2.5 — Fix Consolidator
WHY IT'S NEEDED
⚡ Duplicate Fixes
Agents 2 & 4 both suggest registering the same tech cell — one fix is wasted.
🔀 Instance vs Module
Violation path uses instance name, but CDC tool needs module name for custom sync.
🔍 Shallow Trace
Agent stopped at UMCSYNC wrapper — didn't trace to leaf cell (SYNC3 → two_dff).
WHAT IT DOES
✓ Reads ALL RTL analyzer JSON for its check type
✓ Removes duplicate fix suggestions
✓ Resolves instance → correct module name
✓ Verifies tech-cell traces to leaf level
✓ Writes one unified, deduplicated fix set
SPAWN WHEN
CDC if focus > 0 → data/<tag>_consolidated_cdc.json
RDC if focus > 0 → data/<tag>_consolidated_rdc.json
Lint if focus > 0 → data/<tag>_consolidated_lint.json
SpgDFT if focus > 0 → data/<tag>_consolidated_spgdft.json

## Slide 9: Analyze-Fixer Mode — Auto-Fix Loop
PER-ROUND FLOW
0
Build fix_history from all previous rounds
1
Run full analysis pipeline (Waves 1→2.5)
2
Fix Implementor — apply all fixes
2b
Deep-Dive Agents — resolve 'investigate' items
3
Compile round HTML report
4
Send round email
5
Check termination — loop or stop
TERMINATION STATES
✅ CLEAN
focus_violations == 0
⚠ STALLED
No new fixes applied
🔴 MAX ROUNDS
Round >= 5
WHAT GETS AUTO-APPLIED
CDC/RDC constraint → project.0in_ctrl.v.tcl
CDC/RDC rtl_fix → insert synchronizer in src/rtl/
Lint rtl_fix / tie_off → src/rtl/
SpgDFT constraint → project.params
SpgDFT rtl_fix → path as-is (stable)

## Slide 10: Reliability — Agent Forgetting Prevention
As agents accumulate RTL content their context fills up — critical rules can be displaced. Two layers defend against this.
🛡 Layer 1
CRITICAL_RULES.md — Prevention
config/analyze_agents/shared/CRITICAL_RULES.md (≤25 lines)
Read by orchestrator at startup → stored as CRITICAL_RULES_BLOCK
Prepended at TOP of every sub-agent prompt
Rules: p4 edit ONLY for src/meta/tools/ (never src/rtl/)
Rules: CDC/Lint RTL paths → src/rtl/ (publish_rtl/ wiped each rerun)
Rules: SPG_DFT RTL path as-is (publish_rtl/ stable for SpgDFT)
Rules: Output JSON MUST be written to disk with Write tool
Rules: Fix Implementors run SEQUENTIALLY for full_static_check
Rules: ZERO waivers across all check types
🔄 Layer 2
Output Validation + Retry — Recovery
After every sub-agent completes, orchestrator checks:
ls data/<tag>_<expected_output>.json
EXISTS → proceed to next step normally
MISSING → re-invoke agent once with ⚠️ RETRY message
Still missing after retry → log 'STEP FAILED', continue best-effort
Each agent MD ends with a SELF-CHECK block:
• Did you write your output JSON?
• Did you avoid p4 edit on RTL files?

## Slide 11: File-Based Storage & Fix History
INTERMEDIATE FILE NAMING
data/<tag>_precondition_cdc.json
← CDC/RDC Precondition
data/<tag>_extractor_cdc.json
← CDC/RDC Extractor
data/<tag>_extractor_lint.json
← Lint Extractor
data/<tag>_extractor_spgdft.json
← SpgDFT Extractor
data/<tag>_rtl_cdc_<N>.json
← CDC RTL Analyzer
data/<tag>_rtl_lint_<N>.json
← Lint RTL Analyzer (per file)
data/<tag>_consolidated_cdc.json
← Fix Consolidator CDC
data/<tag>_fix_applied_cdc.json
← Fix Implementor
data/<tag>_deepdive_<N>.json
← Deep-Dive Agent
data/<tag>_analysis_cdc.html
← Report Compiler
FIX HISTORY — Round Memory
Round 1: fix_history = {}
Round 2: fix_history = {
"signal": [{round:1, fix:"rtl_fix",
status:"applied"}]
}
Round 3+: same signal → try different
2+ failures → "investigate"
WHY FILE-BASED?
✓ Survives context interruption — no findings lost
✓ No context bloat — compilers read only what they need
✓ Resumable — partial analyses can be continued
✓ Auditable — each agent's raw output inspectable
✓ Parallel-safe — each agent writes its own file

## Slide 12
Summary
4 Entry Points
Run+Analyze · Only · Fixer · Fixer-Only
4-Wave Pipeline
Extract → Gate → Analyze → Consolidate → Report
Parallel Agents
N agents simultaneously — one per violation/file
File-Based
JSON on disk — resumable, auditable, crash-safe
Auto-Fix Loop
Up to 5 rounds — CLEAN / STALLED / MAX ROUNDS
ZERO Waivers
All violations fixed in RTL or constraints only
Reliability
CRITICAL_RULES.md + output validation + retry
CHECK TYPES
CDC / RDC
Clock/Reset Domain
Crossing analysis
Lint
RTL code quality
violation analysis
SpgDFT
Design-for-Test
violation analysis